        ASSEMBLY

Here we are writing assembly code for counter
whenever counter triggers 101 then extra led will glow

A	B	C	LED
0	0	0	0
0	0	1	0
0	1	0	0
0	1	1	0
1	0	0	0
1	0	1	1
1	1	0	0
1	1	1	0

Code:

.include"/storage/self/primary/Download/FWC/fwc-1/assembly/piosetup/m328Pdef/m328pdef.inc"
ldi r21,0b00000111
out DDRB,r21
ldi r24,0b00000100
out DDRD,r24
ldi r22,0b00000000
ldi r23,0b00000001
loop:
add r22,r23
cpi r22,0b00000101
breq check
cbi PORTD,2
cpi r22,0b00001000
brne rst
ldi r22,0b00000000
check:
mov r24,r22
out PORTD,r24
rjmp rst
rst:
mov r21,r22
out PORTB,r21
call wait
wait:
   push r16
   push r17
   push r18
   ldi r16,0x50
   ldi r17,0x00
   ldi r18,0x00
w0:
  dec r18
  brne w0 ;loop breaks after running 256 times
  dec r17
  brne w0 ;loop breaks after running 256 times
  dec r16 brne w0 ;loop breaks after running 80 times
  pop r18
   pop r17 pop r16
  rjmp loop

connections:
ldi – means load the data
DDRB means port B (connect arduino 8,9,10 pins Led s)
DDRD means port D(connect arduino 4th pin to extra Led)
load 00000000 to register 22
load 00000001 to register 23
inside loop we are adding 22 and 23 registers
then we have to compare with 00000101 then break check then extra led glow
after that increment then reaches to 00001000 then reset to 00000000