        KMAPS
A Karnaugh map (K-map) is a pictorial method used to minimize Boolean expressions without having to use Boolean algebra theorems and equation manipulations.

Increment Decoder:

Without using Don’t cares

Z	Y	X	W	D	C	B	A
0	0	0	0	0	0	0	1
0	0	0	1	0	0	1	0
0	0	1	0	0	0	1	1
0	0	1	1	0	1	0	0
0	1	0	0	0	1	0	1
0	1	0	1	0	1	1	0
0	1	1	0	0	1	1	1
0	1	1	1	1	0	0	0
1	0	0	0	1	0	0	1

Expressions:

A = !W!X!Y!Z + !WX!Y!Z + !W!XY!Z + !WXY!Z + !W!X!YZ

B = W!X!Y!Z + !WX!Y!Z + W!XY!Z + !WXY!Z

C = WX!Y!Z + !W!XY!Z + W!XY!Z + !WXY!Z

D = WXY!Z + W!X!Y!Z

for A:
        yz

        wx 00 01 11 10

1	1		1
1	1		1

A = !W!Y + !WY!Z

for B:
        yz

        wx 00 01 11 10

1			1

1			1

       B = !WX!Z + W!X!Z

for C:
        yz

        wx 00 01 11 10
 1
			1
			1
1
			1

        C = WX!Y!Z + !XY!Z + !WY!Z

For D:

        yz
        wx 00 01 11 10
 1
 1

   D = WXY!Z + !W!X!YZ

 Code:

//Declaring all variables as integers
int Z=0,Y=0,X=1,W=1; // int Z,Y,X,W
int D,C,B,A;

//Code released under GNU GPL. Free to use for anything.
void disp_7447(int D, int C, int B, int A)
{
  digitalWrite(2, A); //LSB
  digitalWrite(3, B);
  digitalWrite(4, C);
  digitalWrite(5, D); //MSB

}
// the setup function runs once when you press reset or power the board
void setup() {
    pinMode(2, OUTPUT);
    pinMode(3, OUTPUT);
    pinMode(4, OUTPUT);
    pinMode(5, OUTPUT);
    //pinMode(6,OUTPUT);
    //pinMode(7,OUTPUT);
    //pinMode(8,OUTPUT);
    //pinMode(9,OUTPUT);
}

// the loop function runs over and over again forever
void loop() {
  //W = digitalWrite(6);
  //X = digitalWrite(7);
  //Y = digitalWrite(8);
  //Z = digitalWrite(9);
  A=(!W&&!Y || !W&&Y&&!Z);
  B=(!W&&X&&!Z || W&&!X&&!Z);
  C=(W&&X&&!Y&&!Z || !X&&Y&&!Z || !W&&Y&&!Z);
  D=(W&&X&&Y&&!Z || !W&&!X&&!Y&&Z);

disp_7447(D,C,B,A);
}

OUTPUT:

With Don’t care Conditions:

Z	Y	X	W	D	C	B	A
0	0	0	0	0	0	0	1
0	0	0	1	0	0	1	0
0	0	1	0	0	0	1	1
0	0	1	1	0	1	0	0
0	1	0	0	0	1	0	1
0	1	0	1	0	1	1	0
0	1	1	0	0	1	1	1
0	1	1	1	1	0	0	0
1	0	0	0	1	0	0	1
1	0	0	1	x	x	x	x
1	0	1	0	x	x	x	x
1	0	1	1	x	x	x	x
1	1	0	0	x	x	x	x
1	1	0	1	x	x	x	x
1	1	1	0	x	x	x	x
1	1	1	1	x	x	x	x

for A:
        yz

        wx 00 01 11 10

1	1	X	1
1	1	X	1
	X	X
	X	X

A = !W

for B:
        yz

        wx 00 01 11 10

		X
1		X	1
	X	X
1	X	X	1

       B = !WX!Z + W!X

for C:
        yz

        wx 00 01 11 10
 1

		X	1
		X	1
1	X	X
	X	X	1

        C = WX!Y!Z + !XY + !WY

For D:

        yz

        wx 00 01 11 10
1	X
	X
X	X	1
X	X

   D = WXY+ !XZ

code:

//Declaring all variables as integers
int Z=0,Y=0,X=0,W=0; // int Z,Y,X,W
int D,C,B,A;

//Code released under GNU GPL. Free to use for anything.
void disp_7447(int D, int C, int B, int A)
{
  digitalWrite(2, A); //LSB
  digitalWrite(3, B);
  digitalWrite(4, C);
  digitalWrite(5, D); //MSB

}
// the setup function runs once when you press reset or power the board
void setup() {
    pinMode(2, OUTPUT);
    pinMode(3, OUTPUT);
    pinMode(4, OUTPUT);
    pinMode(5, OUTPUT);
    //pinMode(6,OUTPUT);
    //pinMode(7,OUTPUT);
    //pinMode(8,OUTPUT);
    //pinMode(9,OUTPUT);
}

// the loop function runs over and over again forever
void loop() {
  //W = digitalWrite(6);
  //X = digitalWrite(7);
  //Y = digitalWrite(8);
  //Z = digitalWrite(9);
  A=(!W);
  B=(!W&&X&&!Z || W&&!X);
  C=(W&&X&&!Y&&!Z || !X&&Y || !W&&Y);
  D=(W&&X&&Y || !X&&Z);

disp_7447(D,C,B,A);
}

Output: